## Slide 1
Gearbox and Bearing Maintenance
Theory Presentation
This document has been created as part of the wider T-shore project, co-funded through the European Union’s ERASMUS+ programme.
Funded by the European Union. Views and opinions expresse are however those of the author(s) only and do not necessarily reflect those of the European Union or the European Education and Culture Executive Agency (EACEA). Neither the European Union nor EACEA can be held responsible for them.

## Slide 2
Document Information
Version no. | Date | Description of changes | Prepared by
01 | 11.12.2024 | New presentation created | Krzysztof Komorowski
Document Author Partners: Fagskolen Rogaland, Energy Innovation, Dalane college
Copyright
This document was developed under the T-shore project, coordinated by Skilliant. © 2024 – Skilliant. All rights reserved. Licensed to the European Education and Culture Executive Agency (EACEA) under conditions.

## Slide 3
Aims and Objectives of Gearbox & Bearings theory
Main Aim
The aim of this theory material is to provide an introduction to the technical knowledge related to gears, bearings, and gearboxes. Additionally, it includes elements of safety when working with mechanical devices and specialized knowledge on the use of gearboxes in wind turbine generators, as well as the topic of gearbox maintenance within the wind energy industry.

## Slide 4
Content

## Slide 5
Mechanical Safety
Lesson 1

## Slide 6
  Safety First
  Doing it Right
  Consistency
  Building a Safety Culture
  Regular Training and Updates
Importance of Approved Working Practices

## Slide 7
Safety data sheets
Material Safety Data Sheets (SDS)

## Slide 8
Safety signs

## Slide 9
PPE when working with mechanics
  Main mechanical PPE equipment:
  Head Protection (Helmets)
  Eye and Face Protection (Safety Glasses and Shields)
  Hearing Protection (Earplugs or Earmuffs)
  Hand Protection (Gloves)
  Foot Protection (Safety Shoes)
  Respiratory Protection (Masks or Respirators)
  Body Protection (Work Clothing and Aprons)
  Fall Protection (Harnesses and Lanyards)
  Personal Protective Equipment (PPE) is essential in providing a barrier between the worker and hazards in the mechanical work environment

## Slide 10
Lockout-tagout procedure

## Slide 11
The importance of appropriate isolation
  The importance of emergency stop buttons…why are they there and when should they be used?
  Impact of e-stop on mechanical systems (video)

## Slide 12
Introduction to Gears
Lesson 2

## Slide 13
Gear definition
  Gears are...
  mechanical devices designed to transmit power between shafts.
  Rolling cylinders or cones with teeth that engage with another cylinder or cone with teeth.
  Power transmission is a crucial aspect of turbine design.

## Slide 14
Gears function
  Forces are transmitted continuously as teeth engage at a constant angle.
  Transfers forces between shafts while changing:
  Rotational speed
  Torque
  Direction of rotation
  Gear application depends on shaft positioning.

## Slide 15
Gears purpose
  Gears purpose:
  To change the direction of rotation
  To modify rotational speed
  To drive multiple machines or outputs
  To synchronize processes
  Used in hydraulics and lubrication pumps

## Slide 16
Types of drive systems
  Open gear:
  Exposed to external contamination.
  Covers may provide some protection.
  Grease-lubricated, typically used in motors, lathes, textile machines, conveyors, and packaging machines.
  Closed gear
  Enclosed in a casing.
  Has a sealed lubrication system.
  Protected against external contamination.
  More durable than open gears.

## Slide 17
Gears functionality
  Smallest gear = Pinion.
  Largest gear = Gear.
  High gear - when a gear drives a pinion.
  Less torque, but more speed
  Speed ​​increases.
  Low gear - when a pinion drives a gear.
  Less speed, but more torque.
  The speed is reduced.

## Slide 18
Gears specification
  Gears and teeth
  They have the same size and tooth design.
  They are manufactured together.
  They are intended to be used together.
  Mechnical advantages
  A reduction in speed leads to an increase in torque.
  Large gears provide a mechanical advantage over smaller gears.
    They rotate over larger surfaces.
    A greater radius offers larger surfaces to distribute forces.
  Internal gears
  The teeth are located on the inner diameter.
  Multiple teeth are in contact at the same time.
  The teeth can be Spur (cylindrical) or Helical (screw-shaped).

## Slide 19
Gears movement
  Radial Shafts
  Refers to the centerline of the gear or shaft.
  Axial and Radial
  Axial movement should ideally be less than zero to maintain stability.
  Support bearings are used to manage both axial and radial forces.
  Axial movements
  Occurs when a gear or shaft can move axially (along its axis) within the bearings.

## Slide 20
Gear tooth profile
  Tooth profile - the profile or design of the tooth is the most important aspect of a gear.
  The profile of the tooth is based on the force curve in the gear.
  The profile also helps to place the forces where the tooth can absorb large forces.
  This contributes to transferring forces between shafts in a smooth manner.
  It also helps extend the lifespan of the gear

## Slide 21
Gears movement
  Driving side of a tooth
  The side of the tooth that drives the engaging tooth.
  The pattern on the contact surface provides a good indication of the gear's position and/or wear.
  Free side of a tooth (coast side)
  The side of the tooth that does not drive the engaging tooth.
The contact surface can be checked using a pain specifically designed for this purpose.

## Slide 22
Power transmission
  Gears can consist of one or more parts. The function is to transfer movement from one shaft to another - Increasing or reducing the revolutions between shafts.
  Changing the direction between shafts may also be desirable.
  Gear transmission is designed based on the placement of shafts and the required gear ratio.
  Often, there is a need to add more gears instead of larger gears

## Slide 23
Gears ratio change
  Direct transmission
  When the input rotational speed is the same as the output rotational speed.
  Driver.
  Power in
  Input gear - engages with the driven gear, causing it to rotate.
  Driven.
  Power out.
  Output gear - rotates as a result of the input gear.

## Slide 24
Gears ratio change
  Increase in Rotational Speed (RPM)
  For gears, the number of teeth is used to calculate the gear ratio
  D in (Input gear diameter) = Ø400 and D out (Output gear diameter) = Ø50.
  Gear ratio =
  Output RPM Formula:
  Output RPM = Input RPM × Gear Ratio
  Example calculations
  If input RPM = 250, what is the output RPM?
  If output RPM = 1500, what is the input RPM?
Output RPM = 250
Input RPM = rpm

## Slide 25
Location of axles
  Gears can be classified based on the positioning of the shafts and how the shafts are connected:
  Parallel shafts: Cylindrical gears, helical gears, herringbone gears.
  Intersecting shafts: Angled teeth.
  Non-parallel, Non-intersecting shafts: Screw versus spiral/helical gears, hypoid gears.

## Slide 26
Gears type
  Common types of gears:
  Spur: Cylindrical gears with straight teeth.
  Bevel: Angled teeth for intersecting shafts.
  Worm: Screw-like gears for high reduction ratios.
  Helical: Spiral-shaped or angled teeth.
  Herringbone: Double helical (fishbone) gears.
  Hypoid: Gears for non-parallel, non-intersecting shafts.

## Slide 27
Cylindrical gears
  This is the most common type of gear.
  Used to transfer power between parallel shafts at moderate speeds.
  Rotational speed: approximately 1000–1500 RPM.
  Features straight teeth that are parallel to the axis of rotation.
  These can be used on both external and internal gears.
Spur gear

## Slide 28
Cylindrical gears
  Rack and pinion
  Used to transfer linear forces to rotary forces

## Slide 29
Cylindrical gears
  Bevel gear
  Often used where shafts cross each other.
  Usually perpendicular
Straight
Spiral

## Slide 30
Cylindrical gears
  Bevel gear
  Develops axial forces and radial forces
  Requires bearings to handle both types of load
  Difficult to set up
    Stable mounting: The shaft is supported by a bearing at each end.
    Unstable mounting: The shaft is supported by a bearing at one end.

## Slide 31
Cylindrical gears
  Hypoid gear - a variant of the bevel gear, Where the teeth are spiral instead of straight.
  Spiral teeth distribute the load over multiple teeth at once.
  This provides smoother operation.
  Transfers forces between two intersecting, non-parallel shafts.
  Bearings are most often pressed onto the shafts.
  Requires extensive lubrication.

## Slide 32
Worm gears
  Worm gear - These are used to transfer power between non-intersecting shafts at right angles.
  Teeth on the worm wheel (gear) have the same profile as cylindrical gears.
  Used for high gear ratios: 7:1 to 70:1 RPM

## Slide 33
Worm gears
  Worm gear specification
  The power comes through the shaft.
  The screw and wheel have teeth that fit together.
  The screw motion of the shaft provides a completely smooth and even output without vibration.
  The sliding of the teeth against each other creates friction, heat, wear, and power loss.
  Greater speed reduction (gear ratio) results in more power loss.60% power loss at a 70:1 gear ratio.
  Requires extensive lubrication.
  Speeds of 3600–6000 FPM.
  The load should not be able to drive the shaft backward.
To determine the gear ratio: One rotation of the screw results in one tooth advancement.

## Slide 34
Helical/spiral gears
  Helical gear - These are used to transmit forces when the shafts are parallel.
  Spiral Angle:
    The angle of the teeth ranges from 7° to 23°.
    The larger the angle, the more teeth are engaged simultaneously.
    The larger the angle, the greater the axial forces become.
    Axial or tapered bearings must absorb these forces.
  Multiple teeth are engaged simultaneously.
    This provides better load transfer and smoother, quieter operation.
    The most common speed range is from 2000 to 2500 RPM.
    Lubrication under pressure is recommended

## Slide 35
Herringbone gears
  Herringbone gear – there are used to transmit forces between parallel shafts.
  There are two rows of inclined teeth, each pointing in a different direction.
  The angle of the teeth is usually 30°.
  These are designed to avoid axial forces.
  They are best suited for high speeds and heavy loads.

## Slide 36
Introduction to Bearings
Lesson 3

## Slide 37
Bearings definition
  Bearings are...
  Machine components designed to reduce friction between moving parts, allowing for smoother motion.
  Bearings support the rotating shafts of the wheels, gears, turbines, rotors, etc. in those machines, allowing them to rotate more smoothly.

## Slide 38
Bearings purpose
  Function 1: Reduce friction and make rotation more smooth
  The main purpose of bearings is to prevent direct metal-to-metal contact between two elements that are in relative motion. This prevents friction, heat generation and ultimately, the wear and tear of parts. It also reduces energy consumption as sliding motion is replaced with low-friction rolling.

## Slide 39
Bearings purpose
  Function 2: Protect the part that supports the rotation, and maintain the correct position for the rotating shaft
  A large amount of force is needed between the rotating shaft and the part that supports the rotation. Bearings perform the function of preventing damage from being done by this force to the part that supports the rotation, and also of maintaining the correct position of the rotating shaft.
  This function of bearings is what allows us to use our machines over and over again for an extended period of time.

## Slide 40
Bearings structure
  Simple structure
  Detailed structure

## Slide 41
Inner Ring / Outer Ring
  The inner and outer ring are usually made from a special high-purity, chrome alloy steel. This material has the necessary hardness and purity – both important factors for a high load rating and a long service life.
  Special materials such as ceramic and plastics are also used. Although plastics cannot withstand extremely high temperatures, they are considerably lighter than steel. This makes them invaluable in sectors such as the automotive industry, where every gram matters.

## Slide 42
Rolling elements
  Rolling elements are either balls, rollers, cones, spheres or needles. They are usually made from a special high-purity, chrome alloy steel. Special materials such as ceramic and plastics are also used.
  The rolling elements roll on the specially formed raceways of the rings or discs and are kept apart and guided by the cage.

## Slide 43
Bearings movement
  Radial bearings / Axial bearings
  Bearings can transmit loads in a radial direction or an axial direction (thrust) and in many cases there is a combination of both radial and axial loads to transmit.
  Radial Bearing
  Axial Bearing

## Slide 44
Bearings movement
  Rolling bearings:
  use rolling elements like balls or rollers to reduce rotational friction, making them ideal for high-speed, low-load applications such as motors and precision machinery
  require minimal maintenance due to their sealed lubrication systems
  Sleeve bearings:
  rely on sliding motion and are better suited for low-speed, high-load applications like industrial pumps and automotive transmissions.
  Due to large contact area need frequent lubrication and replacement under high friction conditions.

## Slide 45
Bearings types
Source: The Engineers Post youtube channel
Notes: Bearings (Mechanical): Know Types, Equations, Advantages, Disadvantages & Applications

## Slide 46
Mounting of bearings
  Bearings can be fitted by the following methods depending on the size and fit of the bearings
  Mounting in a cold condition
  Using a hammer and a length of pipe
  Using hydraulic press
  Around 16% of all premature bearings failures are a result of poor fitting or using incorrect mounting techniques
  Mounting using heat
  Induction heating

## Slide 47
Causes of bearing failure
  Improper lubrication – 43%
  Improper mounting - 27%
  Other lubrication causes – 21%
    Separation in storage
    Temperature limit exceeded
    Moisture contamination
  Fatigue – 9%
  Most bearings fail due to some for of CORROSION

## Slide 48
Introduction to wind turbine Gearbox
Lesson 4

## Slide 49
Gearbox definition
  Gearbox (also called a transmission) is a mechanical device that that is used to increase the output torque or change the speed (RPM) of the motor.
  mechanical unit or component consisting of a gear train or set of gears embedded in a housing – box containing gears

## Slide 50
Gearbox building elements
Gearbox
Bearings
Housing
Lubrication
Accessories
Gears & shafts
Planet gears Parallel gearsets Splines couplings Shafts Keys Mechanical pump gears
CRB TRB Plain bearings Thrust bearings Spherical roller bearings
Torque arm Upper and lower housing Bearing covers Bolts, dowel pins
Lubricant Pumps Filters Valves Coolers Heaters Pipings etc.
Temp sensors Vibration sensors etc.

## Slide 51
Gearbox structure
  Structure of wind turbine gearbox
  housing
  sun gear
  wind turbine's rotor
  planetary arm
  ring gear
  planetary gear (there are a total of three planets gears)
  sun shaft
  wheel,
  middle shaft
  high-speed shaft

## Slide 52
Gearbox structure

## Slide 53
Gearbox structure

## Slide 54
Gearbox structure
  Shafts in gearbox
High speed shaft (HSS)
Input shaft
(Low speed).
Low speed shaft (LSS)
Intermediate shaft (IMS)
Planet gears

## Slide 55
Gearbox structure
  Gears and pinions in gearbox
Intermediate wheel (IMS-wheel)
High-Speed Pinion (HS-gear)
Low speed Gear (LS-gear)
Intermediate pinion (IMS-gear)
Sun pinion
Ring Gear
Planet gear

## Slide 56
Gearbox structure
  Gears and pinions in gearbox
IMS-pinion
HSS-pinion
LSS-wheel
IMS-wheel

## Slide 57
Gearbox structure
  First stage planetary gears

## Slide 58
Gearbox structure
  Intermediate and High-speed parallel stages

## Slide 59
Gearbox structure
  Bearings in gearbox
Intermediate Bearing (IMS-bearing). Rotor side.
High speed bearing (HS-bearing) Rotor side.
High-Speed Bearing (HS-bearing). Generator side.
Intermediate Bearing (IMS-bearing). Generator side.
Low-Speed Bearing (LSS-bearing). Generator side.
Low-Speed Bearing (LSS-bearing). Rotor side.
Planet carrier bearing.
Generator side.
Planet bearings
Planet carrier bearing. Rotor side.

## Slide 60
Lubrication and cooling system
  Main function of lubrication and cooling system
  Reduces friction and wear by introducing a lubricating firm between moving parts
  Helps to dissipate heat away from the critical parts of the equipment
  Facilitates smooth operation of equipment by removing suspending products
  Protection: prevents metal damage due to oxidation and corrosion

## Slide 61
Gearbox in wind turbine

## Slide 62
Role of gearbox in wind turbine
  To multiply the slow speed of the turbine blades (typically 5-15 rotations per minute) to the high speeds (1000 – 1800 rotations per minute) needed to generate electricity using a high speed induction generator
  To transfer power from the low speed turbine shaft at high torque to the high speed generator shaft at low torque
From Blades
Gearbox ratio
To generator
Speed multiplier

## Slide 63
How turbine work
  Conversion of energy
  Rotor Rotation - The rotating blades turn the rotor connected to the main shaft
  Gearbox - increase the rotational speed of the slower-moving main shaft
  Generator - the generator converts the mechanical energy from the rotating shaft into electrical energy.
  Electrical Output – generated electrical power is sent to the power grid for distribution

## Slide 64
Gearbox in wind turbine
Source: Real Engineering youtube channel

## Slide 65
Example of gearboxes in wind turbine
  1,3 MW Gearbox in SWT

## Slide 66
Example of gearboxes in wind turbine
  1,3 MW Gearbox in SWT

## Slide 67
Example of gearboxes in wind turbine
  SWT 3,6-107 (3.6MW) gearbox

## Slide 68
Example of gearboxes in wind turbine
  SWT 3,6-107 (3.6MW) gearbox

## Slide 69
Example of gearboxes in wind turbine
  SWT 3,6-107 (3.6MW) gearbox

## Slide 70
Gearbox Inspection
Lesson 5

## Slide 71
Gearbox maintenance
  Type of Gearbox maintenance
Gearbox maintenance
Unscheduled service
Gearbox service - not working, reduce of efficiency during work, noise in the gearbox, wrong sensors readings
Scheduled service
Proactive inspection – extended inspection with endoscope, check oil level, filters, corrosion etc.
Scheduled inspection – regular schedule maintenance, general visual inspection and check of work conditions

## Slide 72
Gearbox unscheduled service
  Unscheduled service
  Require advance skills, experience and knowledge to solve problem based on initial input and further investigation
  Example service reason:
    Gearbox breakdown – not working
    Reduce working parameters of gearbox - reduce power generation by turbine
    CMS reading in wrong range – vibration sensor, oil temperature sensor etc.
    Noise in the gearbox during operation
    Other reason detected after gearbox scheduled inspection

## Slide 73
Gearbox scheduled service
  Scheduled service
  Require intermediate skills, experience and knowledge to solve problem based on service instruction and manuals
  Example service reason:
    Proactive inspection: Extended inspection to check gearbox condition and condition of specific parts and components. Executed with endoscope for internal parts. Looking for defects, corrosion, oil level, filters and housing.
    Scheduled inspection: regular schedule gearbox check periodicatly (sometimes combine with yearly inspection). General check of work conditions

## Slide 74
Gearbox scheduled service
  Reason of gearbox scheduled service
  Prevent major damage and long downtime for the turbine
  Warranty from the gearbox supplier
  Requirements from insurance companies
  Contract with owner of turbines

## Slide 75
Gearbox scheduled service
  Example documentation of scheduled inspection
Example instructions

## Slide 76
Gearbox scheduled service
  Example documentation of scheduled inspection
Example instructions

## Slide 77
Gearbox scheduled service
  How to take and oil sample for oil analysis
Source: Trico Corporation youtube channel

## Slide 78
Proactive inspection
  Advance internal inspection - borescope

## Slide 79
Proactive inspection
  Advance internal inspection – borescope inspection
Source: EVIDENT Industrial youtube channel

## Slide 80
Proactive inspection
  Advance internal inspection – example borescope inspection
Source: TCGM youtube channel

## Slide 81
Proactive inspection
  Findings example

## Slide 82
Maintenance documentation
  Suggestions how to fill out documentation correctly:
  Ensure all information is completed.
  Use pictures as supporting materials to communicate findings effectively.
  Use only objective and clear communication phrases.
  Double-check serial numbers, part numbers, and other identifiers.
  Use common words and simple expressions for clarity.
  Prioritize findings based on importance or urgency.
  The customer receives a report with all findings.

## Slide 83
tshore.eu@gmail.com
t-shore.eu